## Slide 1: Modularized Robotic Arm
Team 15
Fuhua Song
Kevin Bradshaw
Yuan Tian
Zhengshuai Zhang
Feb 26, 2016

## Slide 2: ICD Presentation Outline
System Interfaces
  Physical Components Overview
  Electrical System Overview
Subsystem Interfaces
  Robotic Arm
  Kinect Control
  Wireless Communication
  Camera Interface
  Hand Tools Integration
Notes: Mechanic Arm System ( load size, # of tools integrated, size, rotation speed, degree of freedom)
Wireless communication system (Data speed, distance)
Power system ( power consumption, heat generated, last time)
kinect Arm Projection Sampling System ( FPS, lag time, recognition ability)

## Slide 3: Physical Components Overview
Robotic Arm
  Weight: 1.6 lbs.
  LxWxH: 19”x2”x4”
  Max weight: 3 lbs.
  Max LxWxH: 26”2”x4”
Robotic Arm
5 Servo Motors
PWM Driver
Raspberry Pi 2
Wireless Module
Power Supply
Laptop
Kinect
Wireless Module
Hand Controller
Feedback Sensors
Modularized Tools
Sensors

## Slide 4: Electrical System Overview
Robotic Arm
5 Servo Motors
16-Channel, 12-Bit PWM Driver
Laptop
Kinect
RF Module
Modularized Tools
Sensors
Raspberry Pi 2
Hand Controller
External Power Supply
User

## Slide 5: Robotic Arm
Servo Motor 1
Shoulder
16-Channel, 12-Bit PWM Driver
J1 GND
J2 OE
J3 SCL
J4 SDA
J5 VCC
J6 V+
PCA9685A
Input 2.3 - 5.5 V
Raspberry Pi 2
GND J9
GND J6
GPIO3 J5
GPIO2 J3
5V J2
GND J20
5V External Power Supply
Servo Motor 2
Shoulder
Servo Motor 3
Elbow
Servo Motor 4
Wrist
Servo Motor 5
Wrist
PWM
V+
GND
Notes: OE = Output Enable
SCL = Serial Clock Line
SDA = Serial Data Line

## Slide 6: Kinect Control
Kinect
User
Laptop
Raspberry Pi
Infrared Rays
Digital over USB
Maximum Sampling Rate: 30 FPS
Default Operation Range: 2.6 ft - 13 ft
Maximum Resolution: 1. Color: 640*480
2. Depth: 320*240
Notes: Use color-coded arrows or ellipses to highlight the Mechanical, Electrical and Thermal Interfaces of SUB-System4. DO NOT change the color-coding of SUB-System4 Functional Block Diagram (if possible).

## Slide 7: Wireless Communication
Arm
Kinect
Camera Interface
User Glove
Sensor
Laptop
Raspberry Pi 2
Arduino Duo
Operation: USB Transmitter/Receiver with antenna via Wifi
Constraints: Lag Time, Synchronization, Integration
Digital
Camera Serial
Interface
USB Serial
Digital
Digital
Notes: Use color-coded arrows or ellipses to highlight the Mechanical, Electrical and Thermal Interfaces of SUB-System1. DO NOT change the color-coding of SUB-System1 Functional Block Diagram (if possible).

## Slide 8: Camera Interface
Laptop
Miniature Camera
Raspberry Pi 2
Camera: Connected to CSI linked to Raspberry Pi 2 GPU send back to computer
Constraint: Latency is primary concern due to visual processing
Resolution: 380 lines
Operation Range:150-foot
Output Frequency: 2.45GHz
Power Supply: 9V Battery
Notes: Use color-coded arrows or ellipses to highlight the Mechanical, Electrical and Thermal Interfaces of SUB-System2. DO NOT change the color-coding of SUB-System2 Functional Block Diagram (if possible).

## Slide 9: Hand/Tools Integration
Touch
Sensors
Raspberry Pi 2
Laptop
Encoder
User
DPDT Switches
12 bit Transmitter RF
Module
12 bit Receiver RF Module
Sensors (typical data values):
Digital Value Resolution: 11 bits - 14 bits
Power Supply: 6 V
Current Supply: ~200 uA
Motor Drive
Tool Motor
Notes: Use color-coded arrows or ellipses to highlight the Mechanical, Electrical and Thermal Interfaces of SUB-System3. DO NOT change the color-coding of SUB-System3 Functional Block Diagram (if possible).

## Slide 10: Conclusion
System Interfaces
  Kinect 1 vs. Kinect 2
  Real time arm movement
  Wireless Communication
Subsystem Interfaces
  Modularized tool applications
  Mechanical Constraints
Thank You!