## Slide 1: Modularized Robotic Arm Team 15 Functional Specification Requirements
Fuhua Song
Kevin Bradshaw
Zhengshuai Zhang
Yuan Tian

## Slide 2: Overview
Modularized Robotic Arm
Functional Systems
  Power and Control Systems
  Wireless System
  Overall System Latency
  Tools/Hand Control System
  Mechanical Systems
ECEN 403 - Team 15

## Slide 3: Power and Control Systems - Kevin
Robotic Arm Power Requirement: 1.5 Hours of Run time
  Power Supply: 12V, 5 ah
  Power Draw: 7.728 W
  Life: 3 hours run time maximum
Raspberry Pi Power Requirement: 2 Hours of Run time
  Power Supply: 5 V, 5 ah
  Power Draw: 6 W
  Life: 4 hours run time maximum
 | Shoulder Motor 1 | Shoulder Motor 2 | Elbow Motor | Wrist Motor 1 | Wrist Motor 2
Current Drain | 700 mA | 350 mA | 230 mA | 180 mA | 150 mA
Power | 3.36 W | 1.68 W | 1.104 W | 0.864 W | 0.72 W
ECEN 403 - Team 15
3

## Slide 4: Wireless System, Raspberry Pi 2 - Fuhua
Wireless Capabilities
  Code simplification to reduce time from MCU
  10+ meter range for prototype phase
  Raspberry pi 2 platform feeding information at 2.4 Ghz wifi
  RF module sending 433Mhz from button to control of the tools
  Raspberry pi send and receive information from laptop as central port
Raspberry pi 2
  Maximum Specification: 900 MHz CPU / 1GB RAM
Raspberry Pi 2 | Module | Used RAM
First Module | Temperature/Haptic Fieldback | <50MB
Second Module | 2 Video System | 150MB
ECEN 403 - Team 15
Notes: Raspberry pi 900 MHz Camera module:RPI_5MCAMWD_LR2

## Slide 5: Latency Minimization- Yuan
Kinect Servo Motor
ourframe.SkeletonData[i].SkeletonPositions[NUI_SKELETON_POSITION_HAND_RIGHT].x
  X,Y,Z coordinate value of 3D map over human joints (“Double” type Size: 8 bytes)
  Numerical Value Ranging from -0.8 to +0.8 (6 feet away from Kinect)
  Coordinate data is processed by a specific algorithm, then is sent to PWM on raspberry Pi 2, which will generate pulses to drive the motor. Algorithm calculation is done by PC which has very high CPU Clk frequency so that the processing time can be neglected.
  Generally,the default PWM frequency is set to be 19.2 MHz (prescale function: pwmClock() ). 100% duty cycle is uniformly distributed over 180 degree. 1.8 degree/ 1 percent of increasing duty cycle cycle.
  Based on calculation, the minimum latency from Kinect to PWM on Raspberry Pi 2 is 0.033s. The highest theoretical Servo motor rotation speed is 3.456E9 degrees / sec, which results in a smallest theoretical servo motor action window of 5.2E-8 sec. The lowest theoretical Servo motor rotation speed is 9000 degrees / sec, which results in a largest theoretical servo motor action window of 0.02 sec. Theoretical Latency: 0.053 s ~0.033 s
  Balance torque and rotation speed of servo motor
ECEN 403 - Team 15

## Slide 6: Tools/Hand Controls - Zhengshuai
Functions and capabilities
  Function: medical surgery assistances
  Capability: gripping,cutting, stitching
Sensor data:
  Force sensors:
  Force required to pierce skin: 100 psi = 68.95 N/(cm^2)
  Infrared Temperature sensor incorporated
Wireless
  Haptic feedback
  Temperature feedback
  Video feedback
Sensors’ Requirements
 | Force sensor | Temperature sensor
voltage | 1V(input) | 2.2 ~ 3.6 V (supply)
current | 2.5mA (max) | 240 uA (max)
ECEN 403 - Team 15

## Slide 7: Mechanical Systems - Kevin
Holding Weight Requirement: 2.25 pounds
  Shoulder Motor 1 Torque: 274.96 oz.in. = 1.432 ft. lbs
  Shoulder Motor 2 Torque: 152.75 oz.in. = 0.796 ft. lbs
  Elbow Motor Torque: 106.90 oz.in. = 0.556 ft. lbs
  Wrist Motor 1 Torque: 66.6 oz.in. = 0.347 ft. lbs
  Wrist Motor 2 Torque: 45.82 oz.in. = 0.239 ft. Lbs
  Current Weight: ~1.6 lbs.
  Possible 7 inch modification extension
ECEN 403 - Team 15

## Slide 8: Conclusion
The Robotic Arm Kit system is optimized for usage in the medical field. The various subsystems enables the system to perform accurate operations wirelessly with minimum latency.
ECEN 403 - Team 15

## Slide 9: Questions?